## Slide 1
OPTICAL STANDARDS & MEASUREMENTS // STD-PRJ-01
PROFESSIONAL PROJECTOR CALIBRATION SUITE
Standard operating procedures for optical convergence, geometry alignment, chromatic balancing, and thermal maintenance.
COMPLIANCE: SMPTE / ANSI standards CALIBRATION SUITE: Geometry, Luminance, Colorimetry, Airflow TARGET PRECISION: ±1% Color Accuracy, Zero Pixel Artifacts
OPTICAL PATHWAY & ANGLE OF PROJECTION
PROJECTION SURFACE (Flat / Uniform Gain)

## Slide 2
01 / GEOMETRIC ALIGNMENT
Geometric Alignment: Aspect Ratios & Keystoning
GEOMETRIC ALIGNMENT PROTOCOLS
[ ] Aspect Ratio Verification: Ensure the source signal aspect ratio matches the projector's native panel layout (e.g., 16:9 widescreen, 16:10 WUXGA, or legacy 4:3) to prevent scaling stretch.
[ ] Physical Leveling & Tilt: Adjust the physical mount's pitch, roll, and yaw faders to align the projection axis perpendicular to the screen surface.
[ ] Optical Lens Shift: Centering the image vertically and horizontally using mechanical or motorized lens shift controls before applying digital correction.
[ ] Keystone Correction: Keep digital keystone processing to absolute minimum (ideally zero) to eliminate pixel interpolation, image compression, and scaling artifacts.
KEYSTONE DISTORTION GEOMETRY
Vertical Keystone Distortion (Uncalibrated)
Orthogonal Calibration (Uniform Grid Alignment)

## Slide 3
02 / OPTICAL LUMINANCE
Luminance: Brightness & Contrast Calibration
LUMINANCE CALIBRATION PROTOCOL
[ ] Black Level (Brightness): Use a standard PLUGE (Picture Line-Up Generation Equipment) test pattern to adjust brightness until dark gray bars are just visible and black bars blend.
[ ] White Level (Contrast): Adjust contrast levels to ensure white details do not clip (crush whites) and details in highlight zones remain distinct.
[ ] Lux & Ambient Light Check: Measure room lux levels with curtains closed. Configure lamp output mode (Normal, High, or Eco) to optimize the dynamic contrast ratio.
[ ] Lamp Degradation Logging: Check current lamp hours against manufacturer expectancy to track gradual decline in lumen output and schedule replacement.
GRAYSCALE STEP CALIBRATION PATTERN
0% (Black)
25%
50%
75%
100% (White)
CALIBRATION METHODOLOGY: 1. Adjust brightness until 0% blends with background. 2. Adjust contrast until 100% is distinct from 75%. 3. Verify color neutrality across mid-tones (25%-75%).

## Slide 4
03 / OPTICAL FOCUS
Clarity: Focus & Optical Panel Convergence
FOCUS & CONVERGENCE CHECKS
[ ] Center & Corner Focus: Project a high-resolution grid pattern. Adjust center focus to sharp limits, then evaluate corner focus to ensure minimal lens aberration.
[ ] Panel Convergence Sweep: Align LCD, LCoS, or DLP red, green, and blue panels to eliminate color fringing (chromatic aberration) on high-contrast text borders.
[ ] Sharpness Verification: Adjust the digital sharpness filter to a neutral value (usually 0) to avoid artificial halos or ringing around characters.
[ ] Analog Clock & Phase: For VGA/Analog inputs, calibrate pixel clock phase to eliminate horizontal crawling noise, jitter, or pixel instability.
OPTICAL ALIGNMENT TARGET GRID
Calibration Standard: The target pattern must display clean, single-pixel white lines. Red, Green, or Blue borders must align within ±0.5 pixels.

## Slide 5
04 / COLORIMETRY
Colorimetry: Color Temperature & Gamut Alignment
COLOR CALIBRATION STEPS
[ ] Color Temperature Selection: Set the baseline color temperature mode to 6500K (D65) for natural, standard-compliant white point representation.
[ ] Color Space Handshake: Confirm the projector's input color gamut setting matches the source video format (e.g., sRGB/Rec. 709 for SDR, Rec. 2020 for HDR).
[ ] RGB Gain & Bias Adjustment: Configure RGB Gain faders (highlights) and RGB Bias faders (shadows) to ensure neutral gray throughout the luminance curve.
[ ] Saturation & Tint Tuning: Fine-tune master color saturation and tint using color bar charts and colorimeters to prevent hue displacement.
REFERENCE CHROMATICITY SWATCHES
RED
GREEN
BLUE
CYAN
YELLOW
MAGENTA
Calibration Target: Rec. 709 Standard Gamut (D65 White Point)

## Slide 6
05 / THERMAL STANDARDS
Thermal Management: CoolDown & Airflow Maintenance
THERMAL & FAN MAINTENANCE
[ ] Filter Maintenance: Clean or replace air filters every 100-300 operating hours to prevent dust accumulation and internal optical engine degradation.
[ ] Air Intake Clearance: Ensure a minimum of 20 inches of clearance around air intakes and exhaust vents to allow unobstructed heat dissipation.
[ ] High Altitude Mode: Enable High Altitude fan profiles when operating above 4,900 feet to compensate for thinner air and prevent overheating.
[ ] Power Down Sequence: Never remove AC mains power directly. Allow the projector to complete its cooling cycle (fans running) to avoid bulb fatigue.
OPTICAL ENGINE THERMAL THRESHOLDS
Component
Normal
Max Limit
Lamp Chamber
75°C - 85°C
95°C
LCD/DLP Prism
45°C - 50°C
60°C
Exhaust Temp
55°C - 65°C
75°C
CRITICAL SAFETY NOTE: Direct AC disconnection cuts off power to cooling fans while the lamp is at max heat, causing immediate panel warping or thermal lamp cracking.

## Slide 7
06 / CALIBRATION LOG
Calibration Log & Quality Certification
VERIFIED CALIBRATION CONDITIONS
[ ] Image Aspect Ratio matches native screen dimensions (16:9/16:10).
[ ] Keystone distortion is eliminated (image edges check perpendicular).
[ ] Focus pattern verified (individual pixels are sharp across grid).
[ ] Grayscale luminance steps are distinct (0% to 100% detail retention).
[ ] Color Temperature checks within target parameters (6500K ±200K).
[ ] Thermal airflow and intake ventilation cleared of obstructions.
CALIBRATION COMMISSIONING SHEET
Projector Manufacturer & Model: ____________________________________________________ Lamp/Laser Engine Run Time Hours: ____________________________________________________ Calibration Instrument Used (e.g., Colorimeter): ____________________________________________________ Commissioning Date: ____________________________________________________ Calibration Technician Signature: X __________________________________________________